## Slide 1
Images downloaded from Spotteron and put into ‘Processed’ (Python)
‘Processed’ images are registered in Photoshop and saved to ‘Registered’
Download
Register
‘Registered’ images are routinely tagged.
(Python)
Tag
Manually remove poorly registered images from ‘Registered’ directory (pretty quick in file explorer)
Refine
Automated
Manual
Either
Timelapse
Shoreline mapping
Statistics

## Slide 2: Tagging
Images in ‘Processed’ are tagged and saved in ‘Registered’
The algorithm iterates backwards from the most recent date, and stops as soon as it finds an image in both ‘Processed’ and ‘Registered’. This will avoid the user from

## Slide 3: Timelapse
Timelapses will be automatically generated for sites based on images in ‘Registered’
Timelapse will be created (scheduled) once/month
Sites can also be run individually, with the user specifying the site name, start date, end date. If no date range is specified, a timelapse will be generated from ‘x’ of the most recent images (‘x’ should be based on how many images required for 1 min timelapse at a quick frame rate).

## Slide 4: Statistics
# processed images
# registered images
# processed images / # registered images = Registration Stability
Registration stability (E.g. Bad, Ok, Good)
Create a script that checks for each site, what images are in ‘Processed’ that aren’t in ‘Photoshop’. Then sorts these by date and picks the latest date and puts into a .csv, next to the site name. Then the user can quickly check the site registration stability and the most recently deleted image date, to know which sites might need to be manually refined.

## Slide 5: Future work
Following up-to-date registration, run the statistics.py script to obtain (# images deleted / # images). This metric should provide an indication of registration stability and in the future, the user will know which sites will require more attention.
Sites that have particularly poor registration may require new target/seed images or a different batch size.